## Slide 1: SIM CARDS
By Theodora Kontogianni
08.02.2011
Seminar Mobile Security
Assigned tutor:
Daniel Loebenberger

## Slide 2: GOAL
SECURITY OF SIM CARDS
=
SECURITY OF CRYPTOGRAPHIC ALGORITHMS

## Slide 3: OVERVIEW
Definition and structure of SIM cards.
A3
A8
COMP128 implementation
A5
Attacks

## Slide 4: Definition and key points
Subscriber Identity Module Cards(SIM Cards)
  A special case of smart cards
  with a microprocessor
  Two major types
    Full size SIM
    Embedded SIM card (for mobile phones)
Embedded SIM card

## Slide 5: Comments on different types of SIM cards
Same thickness on all the types
Same pins
Difference in length and width according to the devices´ needs

## Slide 6: Components of SIM Card
CPU
ROM
EPROM or E2PROM
RAM
Serial communication module

## Slide 7: Important information stored in SIM cards.
Besides SMS and Contacts
Passwords PIN and PUK
International mobile subscriber identity (IMSI)
Integrated circuit card identifier (ICC-ID)
Security authentication (Ki)
Ciphering information (Kc)
And many others!

## Slide 8: Main levels of defence
Prevention of unauthorized access and usage
  PIN (4~8 digits)
  PUK (0~9 digits)
  Local security measure –network not involved
Customer Identity Authentication
  Algorithm A3 (Authentication)
  Algorithm A8 (Cipher Key Generation)
  Both algorithms stored in SIM card
Ciphering of air sent information
  Algorithm A5 (Encryption)
  Embedded in hardware
  New ciphering key (Kc) for each call
  Kc and Ki never transmitted over network
Anonymity
  TMSI sent instead of IMSI

## Slide 9: GSM Architecture
Home Location Register
a
Authentication Center

## Slide 10: A3-GSM Authentication
An 128-bit random challenge(RAND) is generated by HLR and sent to ME.
SIM card encrypts RAND using A3 and Ki stored in SIM card.
A 32-bit response is generated(SRES)
SRES is sent back to the network.
Same operations take place in HLR.
If both SRES are equal then authentication is successful.

## Slide 11: A3 Graphical Overview
A3
Ki
SIM
A3
HLR
128-bit challenge RAND
Mobile Equipment (ME)
Ki
32-bit response SRES
?
Radio Link
If challenges equal then authenticated
IMPORTANT : Ki is never transmitted over the radio link.

## Slide 12: A8-Cipher Key Generation
The same 128-bit random challenge (RAND) used in A3 is the input to A8 also.
SIM card encrypts RAND using A8 and Ki stored in SIM card.
A 64-bit cipher key is generated (Kc).
Kc is used in A5 algorithm.

## Slide 13: COMP128 implementation
A3/A8 are both implemented together in COMP128 since they have the same input.
It was developed in secret so it lacked peer review and testing.
In 1998 a document with its implementation leaked with only a few lines missing that where reverse engineered.
COMP128
128-bit RAND
128-bit Ki
32-bit SRES
64-bit Kc

## Slide 14: COMP128 implementation details
8 rounds – 5 layers
Based on a hash function
Input = 256 bits = 32 bytes= 16 bytes + 16 bytes
Output = 128 – 32leftmost – 64 rightmost = 32 bits
Ki= X[0..15]
RAND= X[16..31]
MAC Adress
Kc

## Slide 15: COMP128- Implementation Details
Order of events
RAND and Ki concatenated in input X[0..31].
The input is hashed 8 times which reduces it from 32 to 16 bytes.
After each hashing but the last the X is permuted.
The output of permutation is the input of the next round.
After 8 rounds the last hash value is the output.

## Slide 16: COMP128

## Slide 17: COMPRESSION-Hash function
Butterfly Structure
16 combining operations of input pair to output pair for each layer.
5 look-up tables Ti (S-box), one for each of the 5 levels i
Each Ti contains 2 9-i (8-i)-bit values
So T0 has 512 8-bit values, T1 has 256 7-bit values and so on....

## Slide 18: Butterfly Structure

## Slide 19: Hash function example
  Example: On level 0 X[ ] is split in X[0..15] and X[16..31]
  The value of each one element of the right part
  (X[i+16]) is combined with each element of the left (X[i]) to compute y= (X[i]+2*X[i+16])mod 512 and z=(X[i+16]+2*X[i])mod 512
  Finally the X[i] = T0[y] and X[i+16] = T0[z]
So the size of elements is reduced from table to table.

## Slide 20: Substitution of Elements

## Slide 21: A5-Encryption
Built-in inside the hardware
3 major versions
  A5/1: the stronger
  A5/2: the weaker
  A5/3: for 3GPP-Kasumi systems
Also secret
Design leaked in 1994
Reverse engineered by Briceno

## Slide 22: A5/1 Logical Details
Conversation in GSM system is a sequence of frames
Each frame is 114 bits from A(ME) to B(Base Station) and 114 bits from B to A.
A5
Kc (64 bit)
Fn (22 bit)
114 bit
XOR
Data (114 bit)
A5
Kc (64 bit)
Fn (22 bit)
114 bit
XOR
Ciphertext (114 bit)
Data (114 bit)
Mobile Equipment
BTS

## Slide 23: System Overview

## Slide 24: Attacs on COMP128
First in 1998 (Smart Card Developer Association)
Exploits weakness in the Butterfly Structure called narrow pipe.
After the second layer of the first round, the output bytes
X[i], X[i+8], X[i+16], X[i+24] depend ONLY on the
input bytes with the same indices.
X[i]=Ki[i] and X[i+18]=Ki[i+18] i=0..7
Size of narrow pipe is 4 bytes.

## Slide 25: Narrow pipe

## Slide 26: Collision
We vary X[i+16], X[i+24]
The rest constant
With chosen text attacks we can hope for a collision.
When collision occurs in round two, it propagates until the last round.
According to the birthday paradox, 214 random challenges are needed to find 2 bytes of Ki[i] and Ki[i+8].
217 chosen texts for the whole Ki

## Slide 27: Other attacks on COMP128
More attacks based on side channels
Partitioning Attack by IBM
Look up table emit data, especially on the first round
8 chosen plaintext

## Slide 28: Conclusion
COMP128 attacks needs 217 queries and possession of the SIM card
SIM cards stop functioning after so many queries
Partitioning attack more than 1000 random challenges
More and more attacks
Companies are afraid of the cost of changing.
Reluctant to put their algorithms under peer review.

## Slide 29
Thank you!
Images on slides 16,18, 20 are modified by
COMP128 : A Birthday surprise